Practical no:7
Layer 2 Security
Network Topology:-

a)Assign the Central switch as the root bridge.

 Assign Central as the primary root bridge.
Using the spanning-tree vlan 1 root primary command, and assign Central as the root bridge

Assign switch13 as a secondary root bridge.
Assign switch13 as the secondary root bridge using the spanning-tree vlan 1 root secondary command.

b)Secure spanning-tree parameters to prevent STP manipulation attacks.
Enable portfast and bpduguard for Access switches for the S3 and S4 :-

Disable BPDU guard on all trunk ports of S1 and S2 to avoid err disabled for unecessary loops state

c) Configure Port Security and Disable Unused Port
S3:-

S4:-

Disable Unused Ports:-

Verify :-

After changing the mac adress for fa 0/4 twice it automatically shutdown

Fast ethernet 0/4 shuts down :-